## Slide 1
India’s only Energy Company in Fortune’s ‘World’s Most Admired’ List
26-27 Nov. 2015
New Delhi
P K Jain
IRS, ONGC
SAARC Training Workshop on Sharing Experience
on
CBM, UCG and Coal Extraction Methodology
Underground Coal Gasification

## Slide 2
UCG Process in general
- Reactions
  - SYNGAS composition
  - Linkage
  - Control
  - Type of Gasifiers
  - Stages in implementation
  - Site selection
  - Site characterization
Utilization of UCG SYNGAS
Indian efforts
Case Histories
Coverage:
33 overseas Assets in 16 countries

## Slide 3
Introduction:
Highest Dividend-paying Company in India
Underground coal gasification (UCG) is the process that can recover the energy of coal seams without the extensive use of traditional mining operations
In UCG, the primary product brought from underground is a Combustible fuel gas of low to intermediate heating content, 100 to 300 Btu/standard cubic foot (scf) (884-2676 Kcal/m3)

## Slide 4
World’s Number 3 Exploration & Production Company : Platts
What is Underground Coal Gasification?
Underground coal gasification (UCG) converts coal / lignite in-situ into a gaseous product, commonly known as synthesis gas or syngas.
UCG Process:
  Drilling of adjacent bore holes in the coal seam.
  Down hole ignition of the coal seam.
  Injection of a pressurised oxidant such as air/oxygen and steam.
  Removal of product gas to surface.

## Slide 5
Growing energy requirement worldwide.
Limited hydrocarbon reserves.
Coal 82% of non-renewables.
India – fourth largest reserves of coal in the world.
Only 20-30% Coal/ lignite mineable. Huge scope for UCG to extract energy from un-mineable coal/ lignite.
Why UCG???
Most valuable Indian PSU

## Slide 6: Total Primary Energy Supply by resource 1993, 2011 and 2020 (Source: WEC Survey of Energy Resources 1995, World Energy Resources 2013 and WEC World Energy Scenarios to 2050)
World Energy Scenario:
A FORTUNE Global 500 Company

## Slide 7
Coal/Lignite resources of India
Coal up to a depth of 1200 m  306 Bt
Lignite reserves
 44 Bt
World’s Number 3 Exploration & Production Company : Platts

## Slide 8
UNMINABLE COAL RESOURCES : 245 BT
UNMINABLE LIGINITE RESOURCES : 39 BT
TOTAL UNMINABLE RESOUCES : 284 BT
RESERVES AMENABLE TO UCG : 10 %
RECOVERABLE RESOURCES : 28.4 BT
UCG GAS (considering 2500 m3/ton) : 75 Trillion m3
CALORIFIC VALUE OF PRODUCED GAS : 3 – 5 MJ / m3
NATURAL GAS EQUIVALENT : 7.5 Trillion m3
CALORIFIC VALUE OF NATURAL GAS : 38 MJ / m3
Potential of UCG in INDIA:
33 overseas Assets in 16 countries

## Slide 9
ONGC a Wealth Creator
Gasification Reaction:
Coal is gasified underground by injecting air or oxygen/steam through Boreholes into a reaction zone formed in the coal seam. The hot gaseous reaction products are Forced to migrate though the coal seam to an exit borehole where they are drawn form underground to the surface. Upon reaching the surface, the gases can be cleaned for direct use as a low-to-medium Btu gas, from upgrading to a substitute natural gas (SNG), or for some other chemical feedstock (SynGas).
Fig. Schematic representation of an underground coal gasification reaction zone
Condensate consisting of phenol, tar, ammonia, carbonic acid, fatty acid, pyridine cynide and thio- cynate etc. is also produced along with syngas
Notes: Condensate consisting of Phenol, Tar, Ammonia, Pyridine cyanide and Thayo cyanide etc. is also produced.

## Slide 10
33 overseas Assets in 16 countries
Growth of UCG Cavity:

## Slide 11
Linking of UCG wells:
World’s Number 3 Exploration & Production Company : Platts

## Slide 12
Ignition of the Coal:
A FORTUNE Global 500 Company
O2 thru Large dia tube.
Inert gas N2 thru small dia tube.
A slug of silane (pyropheric gas) behind the N2.
Methane after silane.
Silane in contact with O2, flame starts.

## Slide 13
# 21 Energy Company in the World
Control parameters – Water, Blast rate

## Slide 14
World’s Number 3 Exploration & Production Company : Platts
Cont…
Effect of gasification rate and water intrusion rate on the heating value of the product gases
Excess water alters the heating value by decreasing the temp. and rate of char reactions and hence altering the gas composition
Effect of gasification rate on heating value at various water injection rates (Edgar and Gregg, 1981). Conversion factor: 1 lb = 0.4536 kg, 1 Btu/ft3 = 37.26 kJ/m3, 1 ft3 = 0.02832 m3.

## Slide 15
ONGC a Wealth Creator
Effect of Seam thickness and Water intrusion on Heating value:
Heat loss from an underground reaction zone to surrounding rock strata is expected to vary inversely with coal seam. In thin seams, temp. may be lower and reaction rates lower. Soviets studies suggest that heating value of the product gas deteriorates rapidly for those seams less than 6’ and gasification cannot sustain in seams less than 3’.
Effect of seam thickness and water intrusion on UCG heating values (Anonn., 1977). Conversion factors: 1 ft = 0.3048m, 1 Btu/ft3 = 37.26 kJ/m3.

## Slide 16
#2 E&P Company in the world
Control parameters – Air OR Oxygen
The use of Oxygen instead of air:
Improves the Calorific Value (CV) of the Product gas, 3-5 MJ/m3 Vs. 13 MJ/m3 in the trial at EI Tremedal.
Improves gasification stability.
Reduces the volume of gas injected.

## Slide 17
A FORTUNE Global 500 Company
Operating Pressure
From an UCG gas generator, at constant air injection rate, a linear relation between gas loss and the difference between the square of the absolute pressure (averaged over the reaction zone) and the square of the atmospheric pressure.
The slope, site specific, is proportional to the permeability of the seam.
Dependence of the relative value of the gas losses on the gas pressure in an underground gas generator (Pitkin, 1960).

## Slide 18
Combustion and gasification products:
Most valuable Indian PSU

## Slide 19
33 overseas Assets in 16 countries
Quality of Product gas:
Oxidising agent (air/ oxygen)
Operating Pressure & Temperature
Feedstock composition
Seam thickness
Moisture content of coal
Oxygen to steam ratio- reducing ratio improves H2 and CH4 while increasing ratio improves CO and CO2.

## Slide 20
Breakthrough of Air/ Oxygen
World’s Number 3 Exploration & Production Company : Platts
Sometimes oxygen in the injected air gets mixed with the product gases prior to it being exhausted from underground , thereby lowering its heating value and also increasing temp. of the production well. The breakthrough or bypass of air/ oxygen often signifies the end of the useful life of the UCG generator.
The data shown are for Hanna II experiment, Heating value and temp. as the function of time.

## Slide 21
Composition of typical dry UCG product gas:
#2 E&P Company in the world
(Calorific Value 13.6MJ/Nm3)
(Spanish Trial-Gasification with Oxygen)
(Angrenskaya – Gasification with Air Injection)
(Calorific Value 3.5 MJ/Nm3)

## Slide 22
UCG syngas vs SCG syngas
World’s Number 3 Exploration & Production Company : Platts
UCG product gas is similar to surface gasifier product. Higher CO2 in UCG signifies the breakthrough of O2.

## Slide 23: Basic design of the controlled retracting injection point (CRIP) system (Hill and Shannon, 1981)
CRIP (Controlled Retracting Injection Point):
Most valuable Indian PSU

## Slide 24
Carbon Energy Bloodwood Trial:

## Slide 25
Schematic Diagram of a Pilot:
#2 E&P Company in the world

## Slide 26
SLANT RIG

## Slide 27
Wellhead:

## Slide 28
How to Proceed
for
UCG Implementation

## Slide 29
UCG implementation Diagram:
Most valuable Indian PSU

## Slide 30
Most valuable Indian PSU
UCG Site Criteria:
Criteria for a suitable UCG site location:
- Geology is key to safeguard environment
- Geologically isolated deep beds
- Deep aquifers should consist of saline, non- potable water & have stratigraphic seals
- Structural integrity & no possibility of cavity roof caving

## Slide 31
A FORTUNE Global 500 Company
Site Selection:
Factors:
Seam thickness
Depth
Coal rank
Ground water
Coal reserve

## Slide 32
End usage of SYNGAS:
#2 E&P Company in the world

## Slide 33
Utilization of UCG SYNGAS:
# 21 Energy Company in the World
Primary product with air as oxidant: low BTU gas, best suited for onsite or near site use as a fuel for boilers, heaters, power generators, and kilns. (80-150 btu/scf )
As low heating value fuel, contains a sizable quantity of inert N2, and hence not cost effective for pipe transportation beyond 1 mile. For onsite use, it is a good source of heat.
Oxygen/ steam : Medium heating value (200-300 btu/scf)- Absence of N2, gas suitable for upgrade thru chemical processing to SNG and/or to several synthesis gas compositions:

## Slide 34
World’s Number 3 Exploration & Production Company : Platts
Up-gradation of Ucg syngas for different end usages:

## Slide 35
General Engineering design for Pilot :

## Slide 36
A FORTUNE Global 500 Company
Basic Processing of SYNGAS:

## Slide 37
UCG – IGCC Power Plant:

## Slide 38
Ammonia Production:

## Slide 39
Fischer Tropsch Process:

## Slide 40
Various companies ONGC, CIL, GIPCL, GMDC, NLC are associated with UCG.
5 Sites (lignite) identified suitable for UCG by ONGC.
Vastan (Gujarat ) lignite block prioritize for UCG pilot.
Detailed Engineering design for pilot is in hand
Block has been awarded by MoC to GIPCL.
ONGC and GIPCL are in process for field trial.
Indian efforts:

## Slide 41
Case Histories:

## Slide 42
A FORTUNE Global 500 Company
UCG – International Scenario 2010:

## Slide 43
World’s Number 3 Exploration & Production Company : Platts
UCG – Worldwide Sites:

## Slide 44
A FORTUNE Global 500 Company
Worldwide UCG Experience Coal Seam Depth & Thickness:

## Slide 45
Current UCG Projects:
Chinchilla UCG project by Linc Energy in Australia.
Carbon Energy UCG project at Surat Basin, Australia.
Eskom Plant in South Africa.
Angren, Uzbekistan Commercial project.
UCG Pilot at Thar, Pakistan

## Slide 46
UCG process started in 1999
The salient features of the UCG process are as follows:
35000 tonnes of coal gasified- more than in any other UCG trial. Within the Rocky Mountain 1 trial- considered the most successful UCG trial in the United States- only 10,000 tonnes were gasified.
80 million Nm3 of gas produced at 4.5-5.7 MJ/m3.
A maximum capacity of 80000 Nm3/hr or 675 tonnes of coal per day was reached at the Chinchilla plant. In comparison, the Rocky Mountain 1 trial achieved a maximum gasification rate of 200 tonnes of coal per day.
The Chinchilla trial proved availability of gas production over 30 months-by far the longest ever recorded outside the ex-USSR.
Chinchilla UCG project by Linc Energy in Australia:

## Slide 47
4 gasifier panels studied.
Directional wells (1 km long) for linkage.
Coiled tubing used for drilling.
Trial with oxygen carried out.
Demo FT facility for aviation fuel using UCG syngas.
De-commissioning of the process –Environment agency vigilant.
Carbon Energy made trial in Blood wood site with oxygen, waiting for permission from Environment agency for commercialization.
UCG projects in Australia:

## Slide 48
Most valuable Indian PSU
Thar-Pakistan:
Thar Block
Lignite reserves: 185 BT, Area: 900 Sq Km, Depth-122-180 m, thickness: 0.3-42 m, Avg. thickness: 21 m
No. of blocks: 12, Two (3 & 5) allocated for UCG
Block 5: 64 sq km, Reserves: 1.4 BT
- 4 coal seams below the casing depth, thickness 0.86 m to 3.58 m, 4 coal seams above the cased depth (130-145 m)

## Slide 49
Thar-Pakistan:

## Slide 50
Initially planned directional drilling, drilling price quoted was 4 times that of whole of the gasifier
Decided to drill vertical wells with reverse combustion technique for linking, total of 36 wells with spacing of 25-30 m as reverse combustion gives satisfactory results in this range
Drilling with 15” bit for 8 ½” OD casing, casing cemented behind to isolate water aquifers at the depth 180-300 ft.
Pilot operated in Dec.’2011
Agencies involved: (i) Pakistan Atomic Energy Commission (PAEC)
(ii) National Engineering & Scientific Commission
(NESCOM)
Thar-Pakistan:

## Slide 51: Difficulties faced
Thar-Pakistan:
In few of the wells of gasifier water aquifer could not be isolated after cementation of the casing
Water level could not be brought down even after excessive pumping
Problematic wells were identified through pump tests and excluded from gasifier

## Slide 52: Thar-Gasifier Layout
52
Layout plan of the gasifier
Permeable water bearing body as intercepted in the gasifier wells

## Slide 53
As per media reports, funds have been approved by Pak Govt. for trial for 10 MW power production
Based on the above results, 100 MW electricity planned to be produced after 3 yrs (As per syngas refiner dated 31st may 2012)
Thar-Pakistan Future Plan:

## Slide 54
Thank You...