## Slide 1
Kamani Jayasekera
Deputy General Manager
Transmission & Generation Planning
Ceylon Electricity Board
Sri Lanka
SAARC Dissemination Workshop
“Designing Management & Monitoring Framework for Regulatory Compliance by Power Transmission Utilities in the SAARC Region”
Country Presentation

## Slide 2
Organization of the Power Sector

## Slide 3: Electricity Data for 2013
Installed capacity - 3334 MW
Peak Demand - 2160 MW
Electricity Generated - 11955 GWh
Generation Mix (2012) - Hydro 28% Thermal 72%
                (2013) - Hydro 57% Thermal 43%
Capacity Mix - Hydro 46% Thermal 54%
System losses - 10.6%
Load Factor - 62.8%
Access to Electricity - 96%
Elec. Consumption per Capita - 515 kWh
Avg. Cost per unit (at selling point) - 17.70 Rs/kWh
Avg. selling price - 18.27 Rs/kWh

## Slide 4: Enhanced accessibility(2013)
Electrification Level in
December 2014
Enrich Life through Power
98%

## Slide 5
EXISTING GENERATING SYSTEM
-
Type | Capacity (MW) | Expected Annual Energy (GWh)
Hydro | 1355 | 4874
CEB Thermal | 848 | 3390
IPP Thermal | 820 | 2605*
NCRE | 311 | 1200
Total | 3334 | 
*Min. Guaranteed Annual Energy

## Slide 6: Hydro Thermal Share
Chart: 
| Hydro | Thermal | Coal | NCRE
 | 0.58 | 0.28 | 0.12 | 0.02
2013

## Slide 7
Chart: Time (GMT+06:00)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
2006 | 808.2 | 711.2 | 744 | 740.3 | 754.2 | 870.7 | 1064.9 | 879.8 | 961.7 | 1161.9 | 1018.5 | 1237 | 1238.5 | 1162.7 | 1173.9 | 1188.9 | 1201.3 | 1166.3 | 1178.1 | 1843.5 | 1849.6 | 1685.2 | 1408.5 | 1055.9 | 891.1
2008 | 799 | 757 | 743 | 729 | 747 | 903 | 1085 | 911 | 1001 | 1227 | 1306 | 1313 | 1348 | 1347 | 1343 | 1344 | 1348 | 1279 | 1268 | 1893 | 1906 | 1785 | 1395 | 1074 | 937
2010 | 923.5 | 897.2 | 871.6 | 876.2 | 884.6 | 1076.9 | 1336.9 | 1135.6 | 1159.1 | 1341.5 | 1435.1 | 1474 | 1479.5 | 1438.9 | 1454.4 | 1504.6 | 1482.4 | 1411.7 | 1365.4 | 1954.7 | 1923.3 | 1750.9 | 1455.9 | 1164.1 | 988.7
2011 | 1044.2 | 1023.3 | 983.7 | 974 | 981.6 | 1162.7 | 1345.6 | 1132.3 | 1250.2 | 1458 | 1543.6 | 1562.7 | 1571.3 | 1503.2 | 1538.4 | 1576.5 | 1551.9 | 1493 | 1396.2 | 2101 | 2134.2 | 1938.5 | 1613 | 1294.6 | 1136.8
2004 | 586.9 | 571.9 | 555.5 | 549.1 | 562 | 655.1 | 871.4 | 960.2 | 847.5 | 943.7 | 992 | 1018.9 | 951.8 | 965.6 | 990.3 | 1008.4 | 996 | 973.5 | 960.4 | 1507.3 | 1523.6 | 1396 | 1087.4 | 825.9 | 704.5
DAILY LOAD CURVE
2134
1923

## Slide 8
Installed Capacity and Peak Demand
Capacity and Demand 2001 -2012
Chart: Per Capita Electricity Consumption
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
Per capita | 289 | 300 | 322 | 348 | 369 | 394 | 414 | 416 | 413 | 449 | 480 | 515
The average per capita electricity consumption in 2012 was 515 kWh/person and generally it has been rising steadily
The installed capacity and available capacity at a time highly depend on machine availability and rainfall

## Slide 9
Chart: National Electricity Peak Demand Forecast (2013-2032)
| 2013 | 2015 | 2017 | 2019 | 2021 | 2023 | 2025 | 2027 | 2029 | 2031 | 2032
Demand (GWh) | 2451 | 2894 | 3193 | 3556 | 3920 | 4287 | 4717 | 5187 | 5625 | 6171 | 6461

## Slide 10
Chart: National Electricity Demand Forecast (2013-2032)
| 2013 | 2015 | 2017 | 2019 | 2021 | 2023 | 2025 | 2027 | 2029 | 2031 | 2032
Demand (GWh) | 11104 | 12834 | 14420 | 16075 | 17830 | 19713 | 21737 | 23932 | 26318 | 28899 | 30258

## Slide 11: Long Term Transmission Development Plan 2013 - 2022
Ceylon Electricity Board
Sri Lanka

## Slide 12
Transmission Planning Procedure
Generation Expansion Plan |  |  | 
YEAR | RENEWABLE ADDITIONS | THERMAL ADDITIONS | THERMAL RETIREMENTS
2013 | - | - | 4x5 MW ACE Power Matara 4x5 MW ACE Power Horana 4x5.63 MW Lakdanavi
2014 | - | 4x5 MW Northern Power 3x8 MW Chunnakum Extension** 1x300 MW Puttalam Coal (Stage II) | 
2015 | - | 1x300 MW Puttalam Coal (Stage III) 3x75 MW Gas Turbine | 6x16.6 MW Heladanavi Puttalam 14x7.11 MW ACE Power Embilipitiya 4x15 MW Colombo Power
2016 | 35 MW Broadlands 120 MW Uma Oya | - | -
2017 | - | 1x105 MW Gas Turbine | -
2018 | 27 MW Moragolla Plant | 2x250 MW Trincomalee Coal Power plant | 4x5 MW Northern Power 8x6.13 MW Asia Power
2019 | - | 2x300 MW Coal plant | 5x17 MW Kelanitissa Gas Turbines 4x18 MW Sapugaskanda diesel
2020 | - | - | -
2021 | - | 1x300 MW Coal plant | -
2022 | 49 MW Gin Ganga | 1x300 MW Coal plant | -

## Slide 13: Present Transmission Network -2013
Transmission voltage levels
  220 kV
  132 kV
Transmission Lines/Cables – 2348 km
  220 kV 502 km
  132 kV 1846 km
      OH 1796 km
      UG 50 km
Grid Substations No | MVA
  132/33 kV 48 3045
  220/132/33 kV 5 2100
  220/132 kV 2 405
  220/33 kV 1 70
  132/11kV 5 369

## Slide 14
2013 Sri Lankan Transmission System

## Slide 15: Cross Border Interconnection with India & Exchange of Power and Harmonization of regulations and Policies
Notes: 15

## Slide 16
Trans-border Electricity Exchange
South Asia Region is very rich in energy resources which are unevenly distributed among the countries of the region.
The advantages of a South Asian Regional Electricity grid are appreciated by almost all countries in the region.
For Sri Lanka to get access to a South Asian Regional Electricity Grid, the only feasible connection is with India through a HVDC marine cable. This interconnection would be different from any other electricity interconnections planned in the South Asia Region.

## Slide 17
Background
    Pre-feasibility study conducted with the assistance of USAID in 2002 by Nexant Inc.
    Review of the Pre-feasibility study with assistance of USAID in 2006 by Nexant/ Power Grid Corporation of India
    Bilateral discussions by Secretary , Ministry of Power and Energy Sri Lanka and Secretary Ministry of Power, India in Dec 2006.
    Cabinet of Ministers approved in principle in Dec 2006, to study the feasibility of power interconnection and to appoint a Steering Committee Co- Chaired by Secretaries of Power Ministries and to appoint a Task Force for technical, commercial, regulatory and legal aspects.

## Slide 18
Background Conts.
A MOU on Feasibility Study for India- Sri Lanka Electricity Grid Interconnection was signed among GOSL, GOI, CEB and Power Grid Corporation of India Limited (PGCIL) on 9th June 2010.
Executing Agencies; CEB and PGCIL are jointly carrying out the feasibility study

## Slide 19: Line Route
Maduari
Panaikulam
130km
Thiruketis
-waram
120km
A’Pura
110km
submarine
overhead
overhead
  High voltage direct current (HVDC), operating at ±400 kV
  Total interconnection capacity will be 1000 MW

## Slide 20: Legal and Regulatory Issues
  CEB needs to be empowered to enter into cross-border power transfers
  The Transmission and Bulk Supply license held by CEB is required to be amended
  Dispute resolution in the Sri Lanka Electricity Act requires to be further strengthened
  CEB Act has to be amended to enable the functions of trader or broker, as relevant

## Slide 21: To achieve project viability
  The project must be structured as a 1x500 MW monopolar interconnection with no specific assets or commitments now to raise the capacity to 1000 MW
  If the project costs are further reduced by reconsidering the routing options, the 1x500 MW monopolar option has the potential to be viable
  Target project cost for a POWERGRID-CEB joint venture to be profitable is 372.4 MUSD (excluding customs duty and taxes), which at present is estimated to be 554 MUSD
  Both Sri Lanka and India be allowed participation in the wholesale market in each others’ country, with full options and freedom to participate in the short-term, day-ahead and unscheduled interchanges market
  Sri Lankan power system shall relax its maximum load share condition and allow the interconnection to supply at the optimal capacity level

## Slide 22: Revised Electricity Grid Interconnection
190 km
50km
140 km
Madurai
New Anuradhapura
Thalai Mannar

## Slide 23
2032 Sri Lankan Transmission System

## Slide 24
Thank You Kamani Jayasekera
Ceylon Electricity Board dgmtgp@ceb.lk