## Slide 1: BHUTAN PERSPECTIVE
Bhutan Power Corporation Limited

## Slide 2: Outline of the Presentation
  Bhutan’s Hydropower Development
  Power Supply & Demand
  Hydrology of Bhutan
  Transmission Network and Export Points
Present Export Arrangements with India
Challenges for cross-border Power Trade for SAARC nations

## Slide 3: Bhutan’s Hydropower Development Salient geographical features of Bhutan
Located in the Eastern Himalayas
Area – 38,394 sq. km
Stretch of 170 km north to south and 300 km east to west
Forest cover – about 72.5%
Altitude range from 200m(south)–7000M(North)
Climate – generally 4 seasons (Spring, Summer, Autumn, and Winter)
Population: 708265(2011)
Religions: Buddhism, Hinduism
Notes: Source: 1. http://www.bhutan.gov.bt/government/aboutbhutan.php
2. http://www.nsb.gov.bt

## Slide 4
Wangchhu Basin(Parochhu, Cherichhu Thimphuchhu etc)
Amochhu Basin(Amochhu-1&2, Cherchhu,Pachhu, Samchhu)
Puntsangchhu Basin(Puna-III,Cherchhu,Dangchhu-1&2,Darachu-1,2&3,Phochu,Mochu etc)
Mangdechhu Basin(Chamkharchu-2&3,Gumthangchu etc)
Drangmechhu Basin(Gamrichu-1,2&3, Komachu, Kuri/Rothpashong etc)
Others(Nyeramari-1&2, Kholong,Aichu,Jaldaka etc)
Bhutan’s Hydropower Development
River Basins of Bhutan

## Slide 5: River Basins identified for Hydropower
Amochhu
Punatsangchhu
Wangchhu
Mangdechhu
Drangmechhu
Others
Notes: Source: NTGMP

## Slide 6: Forest Conservation
70% forest cover
Identified reserve parks and protected areas where development of any sort is restricted
Mostly run off the river hydro power plants to avoid forest destruction and inhabitant displacement

## Slide 7: Hydropower Development in Bhutan
Total Hydro Power Potential = 30,000 MW (Techno-Economically Feasible : 24,000 MW)
Total Installed Hydro Generation Capacity = 1488 MW (from 28 power plants sizes ranging 8 kW to 1020 MW)
First hydropower plant of 360 kW built in 1967 in Thimphu (Capital)

## Slide 8: Existing Major Hydropower Plants (HP)
Sl. No. | Name of Hydropower Plant (HP) | Year of commissioning | Installed Capacity (MW) | Average Annual Generation in (MU)
1 | Chhukha HP | 1986-1988 | 336 | 2,024
2 | Basochhu HP-upper stage | 1999 | 24 | 105
3 | Kurichhu HP | 2000- 2001 | 60 | 400
4 | Basochhu HP-lower stage | 2004 | 40 | 291
5 | Tala HP | 2006-2007 | 1,020 | 4,865
 | Total |  | 1,480 | 7,865
Mini/micro hydel add around 8MW
Notes: Source: Power Data Book 2011, BPC

## Slide 9: Hydropower Development in Bhutan (Contd.)
First CDM (Clean Development Mechanism) micro hydro (Chendebji) – 70 kW commissioned in August 2005
Remaining to be developed = 71 large sites that have been identified ( 22,280 MW)
10,000 MW hydropower generation capacities to be developed by 2020.

## Slide 10: Reservoir HEP
Wangchhu Reservoir (570MW)
Bunakha Reservoir (180MW)
Amochhu Reservori (540MW)
Notes: HEP: Hydroelectric Projects

## Slide 11: Power Supply & Demand
Electricity export - About 75% of the generation
Annual export estimate = 7,216.53 MU (2010)
Revenue from sale of electricity contributes to 40% of national revenue.
Bhutan’s consumption + losses = 1,628.03 MU (2010)

## Slide 12: New Hydro Generating Stations in Bhutan by 2020
Sl. No. | River Basin | Project Name | Installed Capacity (MW) | Year of Commissioning
1 | Punatsangchhu/Wangdiphodrang | Punatsangchhu-I HEP | 1200 | 2015
2 | Punatsangchhu/Wangdiphodrang | Punatsangchhu-II HEP | 990 | 2017
3 | Punatsangchhu/Lhamoizingkha | Sunkosh Main HEP | 2500 | 2020
4 | Punatsangchhu/Lhamoizingkha | Sunkosh Barrage HEP | 85 | 2020
5 | Wangchhu/Chukha | Wangchhu HEP | 570 | 2019
6 | Wangchhu/Chukha | Bunakha Reservoir HEP | 180 | 2020
7 | Amochhu/Samtse/ Chukha | Amochhu Reservoir HEP | 540 | 2018
8 | Punatsangchhu | Dagachhu HEP | 126 | 2015
9 | Mangdechhu/Trongsa | Mangdechhu HEP | 720 | 2017
10 | Mangdechhu/Trongsa | Nikachhu HEP | 210 | 2020
11 | Mangdechhu/Zhemgang | Chamkharchhu-I HEP | 770 | 2018
12 | Drangmechhu/Mongar | Kuri-Gongri HEP | 1800 | 2020
13 | Drangmechhu/Trashiyangtse | Kholongchhu HEP | 600 | 2018
14 | Druk Bindu | Bindu Khola | 13 | 2020
 |  | Total MW | 10,304 | 

## Slide 13
Length of 400 kV D/C lines 74.143 km
Length of 220 kV D/C lines 35.780 km
Length of 220 kV S/C lines 183.739 km
Length of 132 kV S/C lines 344.628 km
Length of 66 kV S/C lines 302.152 km
Length of 66 kV D/C lines 5.960 km
Length of 66 kV M/C lines 3.405 km
Total Transmission Line Length 949.807 km
Existing Transmission Network in Bhutan

## Slide 14: Existing Transmission Substation in Bhutan
Sl. No. | Substation | Qty (Nos.) | Capacity (MVA)
1 | 400 /220/66kV substation | 1 | 200
2 | 220 /66kV substation | 2 | 220
3 | 132kV substations | 7 | 102
4 | 66kV substations | 11 | 199.5
5 | 33kV substations | 1 | 3
6 | 66kV Switching Station | 1 | -
 | Total | 23 | 724.5
Notes: Source : Power Data Book 2011, BPC

## Slide 15: Transmission Network in Bhutan

## Slide 16
Technical
  Use of common corridor (transmission network) versus dedicated transmission pipe
  Requirement of Uniform Standards
  Billing & Metering Issues
  Interaction among the LDCs
  System security of the different grids
  Maintenance of Grid Discipline
Challenges for SAARC Power Exchange

## Slide 17
  Use of common corridor (transmission network) versus dedicated transmission pipe
  Common Corridor may optimize the overall SAARC grid requirements but would require proper mechanism to be put in place for energy exchange mechanism, associated agreements with responsibilities of multiple agencies
  Dedicated transmission pipe would to an extent have simpler mechanism but may not be optimal. Further, jurisdiction for maintenance of the lines and / or any lease for the land occupied by corridor would have to be addressed.
Challenges for SAARC Power Exchange

## Slide 18
  Use of common corridor (transmission network) versus dedicated transmission pipe
  Complexities associated with dedicated transmission pipe less compared to common corridor
  Responsibility fixing relatively easier in dedicated one [However, it should be noted that in the interconnected systems, grid disturbances due to failure of any of the constituents are likely to impact others, even under dedicated transmission pipes]. But ‘external’ disturbances should be duly taken care of in the agreements.
  Common corridor through proper coordinated planning would benefit all and could also be made simpler, if the constituent nations agree for an integrated approach.
  Dedicated transmission pipe would not be feasible for all SAARC region.
Challenges for SAARC Power Exchange

## Slide 19
  Requirement of Uniform Standards
  It is necessary to develop common codes and standards.
  Inter-grid disturbances can be minimized through DC links.
  Individual grid isolation and corresponding transient response of generators to be so as to ensure secured isolation without black-out.
  The voltage and frequency norms should be standardized with due consideration to the already existing generators / infrastructure in each country.
  Interaction and coordination mechanism to be properly developed among constituent grids.
Challenges for SAARC Power Exchange

## Slide 20
  Billing & Metering Issues
  Standardized Billing mechanism (even if rates / tariffs are different) or separate mechanism between different nations / parties.
  Metering and more importantly CT / PT accuracies to be standardized
  Mechanism for joint metering needs to be redefined, possibly with nominated entity (entities) for ease of implementation [Since the energy exchange through the same meters needs to be adjusted / billed to multiple agencies, proper system of power injection with identified recipients for different times of a day, would be necessary].
  Adoption to address critical issues, at least till the power situation improves in the region and there is overall surplus power at any time for meeting the overall SAARC demand. Power-shortage situations, as now, would require more complex mechanisms.
Challenges for SAARC Power Exchange

## Slide 21
  Interaction among the LDCs
  Necessary to establish nodal agencies for each constituent nation, like LDC for each nation, with a central nodal agency (comprising of representatives of multiple nations at the helm and with functional autonomy)
  Institutionalization of proper mechanism for regular data transfer, outage management (including outage scheduling) and functional control
  Financing mechanism for the LDCs
Challenges for SAARC Power Exchange

## Slide 22
  System security Aspects of the different grids
  Need to assess impact on existing intra-nation and inter-nation PPAs
  Penalty fixation may have to consider impacts on constituent nation’s liabilities / obligations to its existing local customers and local regulatory authorities
  Other issues like ‘insulation’ from other inter-nation restrictions due to Govt policies
  Maintenance of Grid Discipline
  Develop systems with all nuances associated with Grid Discipline
Challenges for SAARC Power Exchange

## Slide 23
  Bhutan shares boundary with only India among the SAARC nations and thus any power exchange would be only through India, whether it is dedicated transmission pipes or shared common transmission infrastructure.
  Bhutan’s electricity exchange in the near future is expected to be mostly with India due to overall power shortage with possible power exchanges with other nations limited to periods of surplus power.
Challenges for SAARC Power Exchange

## Slide 24
THANK YOU