## Slide 1: MODALITIES FOR CROSS BORDER CONNECTIVITY AND RELATED OPERATIONAL ISSUES-HVDC AND RADIAL MODE CONNECTIONS
SK SINGH, CHIEF ENGINEER, COMMERCIAL, NBPDCL, INDIA

## Slide 2: EXISTING POWER TRADE-NEPAL
AGREEMENT EXECUTED BETWEEN INDIA & NEPAL.
BIHAR HAS AGREED TO SUPPLY 50 % GENERATED POWER FROM KOSI HEP.
THE PROJECT HAS NOT GENERATED POWER TO ITS RATED CAPACITY
BIHAR THROUGH ERSTWHILE BSEB HAS SUPPLIED 50 % POWER FROM ITS OWN SOURCE TO HONOUR THE INDO NEPAL AGREEMENT.
GOVT. OF INDIA HAS ALLOCATED 50 MW CHEAPER POWER TO BIHAR FOR SUPPLY TO NEPAL
BIHAR IS SUPPLYING MORE POWER i.e. 125 MW DURING EVENING TO NEPAL ON PRIORITY BASIS.

## Slide 3: EXISTING POWER TRADE-NEPAL
PRESENTLY NEPAL IS BEING SUPPLIED POWER THROUGH THE FOLLOWING TRANSMISSION AND SUB TRANSMISSION LINES:
132 KV KATAIYA – KUSAHA (DUHABI) TRANSMISSION LINE
132 KV BETTIAH – BALMIKINAGAR – GANDAK TRANSMISSION LINE
33 KV RAXAUL – BIRGUNJ TRANSMISSION LINE
33 KV SITAMARHI – JALESWOR TRANSMISSION LINE
33 KV JAYANAGAR – SIRAHA TRANSMISSION LINE
33 KV KATAIYA - RAJBIRAJ TRANSMISSION LINE

## Slide 4: EXISTING POWER TRADE-NEPAL
THE EXISTING TARIFFS APPROVED BY INDO NEPAL POWER EXCHANGE COMMITTEE (PEC) FOR 2014-15 EFFECTIVE FROM 1ST APRIL 2014 FOR EXCHANGE OF POWER BETWEEN INDIA – NEPAL AT DIFFERENT VOLTAGE LEVELS ARE AS FOLLOWS:
132 KV KATAIYA – KUSAHA (DUHABI) – RS. 5.05 / KWH
132 KV BETTIAH – BALMIKINAGAR – GANDAK - RS. 5.05 / KWH
33 KV RAXAUL – BIRGUNJ TRANSMISSION LINE - RS. 5.46 / KWH)
33 KV SITAMARHI – JALESWOR TRANSMISSION LINE - RS. 5.46 / KWH
33 KV JAYANAGAR – SIRAHA TRANSMISSION LINE - RS. 5.46 / KWH
33 KV KATAIYA - RAJBIRAJ TRANSMISSION LINE - RS. 3.90 / KWH (SUBSIDIZED RATE I.E. RS. 5.46 PER KWH X 10/14 = RS. 3.90 PER KWH)

## Slide 5: EXISTING POWER TRADE-NEPAL
SUPPLY OF POWER TO NEPAL BEYOND 50 MW ON 132 KV IS CHARGED AT ENERGY CHARGE @ RS. 5.40 / KWH SINCE FINANCIAL YEAR 2013-14 AT 132 KV AS DETERMINED BY BERC.
AS PER THE INDO – NEPAL AGREEMENT, SUPPLY OF POWER TO NEPAL THROUGH 33 KV D/C KATAIYA – BIRATNAGAR (CKT-1 IS UNDER BREAKDOWN AND 33 KV KATAIYA – RAJBIRAJ ARE AT SUBSIDIZED RATE IN THE RATIO 10:14 (KOSI RATE) OF THE NORMAL 33 KV RATE (i.e. RS. 5.46 / KWH).

## Slide 6: EXISTING POWER TRADE-NEPAL
THE DIFFERENCE BETWEEN NORMAL 33 KV RATE & SUBSIDIZED RATE COMES UNDER KOSI DISPUTE WITH NEPAL, WHICH HAS NOT YET BEEN RESOLVED BETWEEN INDIA & NEPAL AND ALSO BY THE MINISTRY OF POWER & MINISTRY OF EXTERNAL AFFAIRS, GOVT. OF INDIA.
BIHAR IS WILLING TO SUPPLY MORE POWER TO NEPAL BEYOND THE EXISTING TRANSACTION AS WELL AS PURCHASE POWER FROM UPCOMING HYDRO PROJECT IN NEPAL.

## Slide 7: EXISTING POWER TRADE-NEPAL
REQUEST MADE BY THE ERSTWHILE BSEB [NOW BSPHCL] TO GOVT. OF INDIA FOR ALLOCATION OF POWER FROM ARUNA-III HEP, NEPAL BEING DEVELOPED BY SUTLUJ JAL VIDYUT NIGAM LIMITED.
THE CONCERN OF BIHAR RELATED WITH PAYMENT OF MINIMUM DEMAND CHARGES BY NEPAL IN CASE OF LESS DRAWL / NO DRAWL OF POWER BY NEA IS ALSO AN ISSUE, WHICH ALSO REQUIRES TO BE ADDRESSED BY THE NEA

## Slide 8: EXISTING POWER TRADE-BHUTAN
BHUTAN HAS A POTENTIAL OF 30,000 MW HYDRO POWER GENERATION CAPACITY OUT OF WHICH ONLY 1.5% HAS BEEN TAPPED TILL NOW.
CHUKHA HYDRO ELECTRIC PROJECT (HEP) OF 336 MW WAS COMMISSIONED IN 1983 WITH FINANCIAL ASSISTANCE OF GOVERNMENT OF INDIA.
THIS WAS FOLLOWED BY SETTING UP OF 60 MW KURICHHU HEP IN YEAR 2002.

## Slide 9: EXISTING POWER TRADE-BHUTAN
TALA HEP OF 1020 MW IS UNDER IMPLEMENTATION AND FIRST UNIT HAS BEEN COMMISSIONED ON JULY 17, 2006.
BIHAR HAS AN ALLOCATION 260 MW & 80 MW FROM TALA & CHUKKA HEP AT THE RATE RS. 2.05/KWH & RS. 1.75/KWH RESPECTIVELY.
BIHAR HAS ALSO REQUESTED FOR ALLOCATION OF 1500 MW POWER FROM PUNATSANGCHU HEP, BHUTAN AND ALSO WILLING TO PARTICIPATE IN THE BIDDING PROCESS FOR PROCUREMENT OF POWER FROM NIKKACHU (118 MW) HEP THROUGH PTC.

## Slide 10: EXISTING POWER TRADE-BHUTAN
INDIA PURCHASES ON AN AVERAGE 300 MW FROM CHUKHA HEP AND 60 MW OF KURICHHU HEP.
IT IS PROPOSED TO PURCHASE THE ENTIRE SURPLUS POWER FROM TALA HEP AFTER ITS COMMISSIONING.
INDIA HAS AGREED TO IMPORT A MINIMUM OF 5,000 MW OF ELECTRICITY FROM BHUTAN BY THE YEAR 2020.

## Slide 11: EXISTING POWER TRADE-BHUTAN
THE AGREEMENT IS TO HAVE A LONG-TERM FRAMEWORK FOR COOPERATION AND ALSO TO OPEN UP COOPERATION TO BOTH PUBLIC AND PRIVATE ENTITIES.
HENCEFORTH, THE COOPERATION WOULD BE MORE ON COMMERCIAL TERMS AND POWER PURCHASE AGREEMENTS ARE BEING SIGNED PRIOR TO THE IMPLEMENTATION OF THE PROJECTS

## Slide 12: OTHER SAARC COUNTRIES- NO TRADE WITH BIHAR
BANGLADESH
INDIA HAS ALSO STARTED SUPPLYING 250 MW POWER TO BANGLADESH FROM EASTERN GRID.
BIHAR MAY OPTION OF SUPPLYING SURPLUS TO BANGLADESH AFTER THE COMMISSIONING OF THE UPCOMING POWER PROJECTS UNDER CENTRAL SECTOR AND LONG TERM PPA WITH IPPS.

## Slide 13: PAKISTAN
PAKISTAN CONFIRMED AVAILABILITY OF ONLY ABOUT 300 MW CAPACITY FOR EXPORT DURING NEXT TEN YEARS AND PROPOSED A TARIFF OF 8.49 CENTS PER UNIT AT 60% LOAD FACTOR AND 6.69 CENTS PER UNIT AT 90% LOAD FACTOR.
INDIA PROPOSED AN ALTERNATIVE ARRANGEMENT OF "TAKE AND PAY" INSTEAD OF "TAKE OR PAY" ARRANGEMENT PROPOSED BY PAKISTAN. THERE HAS BEEN NO FURTHER PROGRESS ON THE MATTER.

## Slide 14: MYANMAR
INDIA HAD EXTENDED ASSISTANCE FOR DESIGN AND ENGINEERING OF SEDAWYGI HEP (25 MW).
IN ADDITION, TAMANTHI HEP (1200 MW) HAS BEEN IDENTIFIED AS A MUTUAL BENEFIT PROJECT.

## Slide 15: MYANMAR
THREE PROJECT SITES HAVE BEEN ESTABLISHED FOR DEVELOPMENT BY INDIA ON CHINDWIN RIVER.
PRE-FEASIBILITY REPORT OF TAMANTHI HEP HAS BEEN PREPARED BY NHPC AND SUBMITTED IN APRIL, 2005.
DPR FOR THIS PROJECT IS NOW PREPARED BY NHPC FOR WHICH AN MOU IS TO BE SIGNED BETWEEN NHPC AND GOVT. OF MYANMAR.
INDIA HAS ALSO ASSISTED MYANMAR BY WAY OF SETTING UP A DEMONSTRATION BIO-MASS GASSIFIER PLANT.

## Slide 16: SRI LANKA
NTPC HAS PROPOSED TO SET UP A COAL-BASED POWER STATION IN SRI LANKA OF 2X250 MW CAPACITY.
THE DISCUSSIONS ON TO FINALIZE MOU.
USAID HAS TAKEN UP A FEASIBILITY STUDY FOR INDIA'S ELECTRICAL GRID INTERCONNECTIONS WITH BANGLADESH AND SRI LANKA.
INDIA AGREED TO THIS STUDY (WHICH IS BEING TAKEN UP BY PGCIL) IN VIEW OF THE CONSENT OF BOTH BANGLADESH AND SRI LANKA FOR THE SAME.

## Slide 17: RELATED OPERATIONAL ISSUES- HVDC-DISADVANTAGES
HVDC GRID INTERCONNECTIONS HAS LIMITED QUANTUM OF POWER FLOW
LIMITED SUPPORT IN PROVIDING BALANCING POWER
THE HIGHER COST OF DC CONVERSION EQUIPMENT COMPARED TO AC SYSTEM.

## Slide 18: RELATED OPERATIONAL ISSUES-HVDC-ADVANTAGES
ALLOWS INDEPENDENT FREQUENCY OPEARTION OF THE CONNECTED GRIDS
DONOT ALLOWS DISTURBANCES TO TRAVEL FROM ONE GRID TO ANOTHER
HVDC AVOIDS THE HEAVY CURRENTS REQUIRED TO CHARGE AND DISCHARGE THE CABLE CAPACITANCE EACH CYCLE. FOR SHORTER DISTANCES.

## Slide 19: HVDC-ADVANTAGES
FOR LONG-DISTANCE TRANSMISSION , HVDC SYSTEMS LESS EXPENSIVE AND SUFFER LOWER ELECTRICAL LOSSES
HVDC ALLOWS POWER TRANSMISSION BETWEEN UNSYNCHRONIZED AC TRANSMISSION SYSTEMS.

## Slide 20: REQUIREMENTS FOR HVDC TRANSMISSION
ACTIVE POWER CONTROL AND FREQUENCY SUPPORT
REACTIVE POWER CONTROL AND VOLTAGE SUPPORT
FAULT RIDE THROUGH
PROTECTION DEVICES AND SETTINGS
POWER SYSTEM RESTORATION

## Slide 21: FOR BIHAR -UNREMUNERATIVE HVDC SYSTEM
REGULATED AND LOW TARIFF RATE.
LOW QUANTUM OF POWER EXCHANGE BETWEEN BHUTAN AND NEPAL DESPITE HIGH POTENTIAL.
UNIDIRECTIONAL POWER FLOW
NON PARTICIPATION OF IPPs.
HVDC FOR CROSS BORDER POWER FLOW IS DESIRABLE BUT VOLUME IS THE BARRIER.

## Slide 22: BIHAR AS REGIONAL HVDC HUB
BIHAR CAN BE HUB FOR CROSS BORDER TRADE IN POWER FOR NEAPL AND BHUTAN.
VOLUME OF TRADE MAY JUSTIFY HVDC SYSTEM DEVELOPMENT TRANSMISSION LICENSEE.
THE PRESENT SYNCRONOUS CROSS BORDER TRADE IN POWER CAN NOT SUSTAIN THE POTENTIAL AVAILABLE WITH NEPAL AND BHUTAN.
WITH INCREASING VOLUME OF TRADE IN POWER LOSSES WILL RISE BEYOND REGULATORY NORMS WITH ACCOMPAYING DANGER OF FAULTS CROSSING THE BOUNDARIES.

## Slide 23: ISSUES FOR BIHAR- OPEN UP THE BOUNDARIES AMONG SAARC COUNTRIES
DEVELOPMENT OF INTERNATIONAL GRID AND GRID CONTROL.
INTERNATIONAL REGULATORY FRAME WORK
REMUNERATIVE TRANSMISSION CHARGES
REMUNERATIVE DEMAND AND SUPPLY
DISPUTE RESOLUTION MECHANISM
DIFFERNTIAL DUTIES AND TARIFF
GENERAL NETWORK ACCESS

## Slide 24
THANKS