## Slide 1: Hydro Projects in Nepal IPP perspective on power trading
Khadga Bisht
President, IPPAN

## Slide 2: Institutional Framework
Ministry of Energy
Investment Board for >500 MW
Water & Energy Commission
Department of Electricity Development
Nepal Electricity Authority
IPP
Distribution
Transmission
Generation

## Slide 3: Power market characteristics
  Small market (6 TWh/a), rapid growth (10-12%)
More than 97% grid connected supply is hydro
60% has access to grid
Both energy and capacity deficit. Dry season supply is about one-third of the demand
  Demand supply mis-match
More than 97% hydro supply,
depends on monsoon.
Higher demand during dry season
Low industrial demand
  Cross Border Market
Nepal importing power from India
Long term plan is to export power to India
CBTL and PTA are pre-requisites
Key take-away:
  Small market (6TWh/a) with rapid growth
  Opening cross-border market with greater opportunities
  Generation mix is highly dominated by Hydro

## Slide 4: “Domestic” projects under construction
Upper Tamakoshi – 456 MW
Chameliya – 30MW
Upper Trishuli IIIA – 60MW
Kulekhani III – 14MW
Marsyangdi A – 50MW
Sanima Mai -22MW
Middle Bhotekoshi – 102MW
Rasuwagadi – 111MW
Sanjen – 15+43=58MW
Modi – 20MW
others
Total Approx: 1200MW
By 2020 Domestic Projects portfolio approx. 2000MW

## Slide 5: Large Project with Export component
Arun 3
900MW
Upper Karnali 900MW
TA3 650MW
Upper Marsyandi 2 600MW
L Arun
400MW
Notes: I’d like to step back and focus on the first stage of regional integration – bilateral trade agreements

## Slide 6: Why Power Trading for IPPs

## Slide 7: Capacity Balance
Year | Dry Season, MW |  |  | Wet Season, MW |  |  | 
 | Gen | Peak | Shortage | Peak | Gen | Shortage | Surplus
2013/14 | 641 | 1242 | 602 | 1217 | 849 | 368 | 
2014/15 | 665 | 1357 | 693 | 1309 | 902 | 407 | 
2015/16 | 940 | 1480 | 541 | 1379 | 1139 | 239 | 
2016/17 | 1001 | 1612 | 611 | 1555 | 1363 | 191 | 
2017/18 | 1694 | 1742 | 48 | 1680 | 1987 |  | 306
2018/19 | 1807 | 1880 | 73 | 1814 | 2217 |  | 403
2019/20 | 1922 | 2027 | 105 | 1888 | 2492 |  | 604
2020/21 | 2016 | 2183 | 168 | 2106 | 2501 |  | 395
Source: NEA

## Slide 8: Energy Balance
Year | Energy, GWh |  |  | 
 | Demand | Generation | Surplus | Deficit
2013/14 | 5,863 | 5,480 |  | 383
2014/15 | 6,406 | 5,766 |  | 640
2015/16 | 6,967 | 7,415 | 448 | 
2016/17 | 7,606 | 8,475 | 869 | 
2017/18 | 8,221 | 12,936 | 4,715 | 
2018/19 | 8,873 | 14,419 | 5,546 | 
2019/20 | 9,539 | 16,160 | 6,621 | 
2020/21 | 10,304 | 16,487 | 6,183 | 
Source: NEA

## Slide 9: Power Trading Possibility
Total theoretical potential: Over 83,000 MW
Economically Feasible potential: 43,000 MW
Storage capacity plants: 21,400 MW
Under Construction : 1200MW
Under PDA: 3000MW
Under Survey: 9000MW
Total Maximum Demand by 2020:4500MW
Export minimum by 2020: 6000MW

## Slide 10: Power System Generation Mix
 |  | Thermal | Hydro | Other
1 | Bangladesh | 95% | 5% | -
2 | Bhutan | - | 100% | -
3 | India | 71% | 25% | 4%
4 | Nepal | 7% | 93% | -
5 | Pakistan | 71% | 27% | 2%
6 | Sri Lanka | 56% | 44% | -

## Slide 11: South Asia – Vibrant Energy Market
Hydro potential from Nepal and Bhutan are seasonal and production peak is synchronized to India’s peak demand
India is fully capable of being the anchor base load with coal
Southern peninsula excellent for wind resources
Pakistan, Bangladesh and Myanmar are equipped for flexible generation fired on Gas
Expanding the Power and Gas grids also gives countries a potential to develop previously undeveloped resources for common utilization
Synergies are there to be explored and developed
Hydro & NG
Hydro
Coal
Natural Gas
Hydro
Wind
Wind
Notes: The sheer size of the Energy market that can evolved out of regional cooperation is mind boggling – an energy market serving a population of 1.5billion people with annual energy demand approaching 1,000 TWh – I am not going to guess how many zeroes there are behind that number, it’s dizzying. pronounced differences in in energy endowments and energy consumption among the countries in the region and the win-win opportunity regional trade offers

## Slide 12: Regional Power System
UCTE
GCC
PJM
GMS
SIEPAC
Brazil-Uruguay -Argentina
SAPP
NT2
Manatali

## Slide 13: Existing Interconnections with India
Transmission Link | Evacuation Cap. (MW) | Traded, MW | Voltage Level, kV
Kusaha--Kataiya | 130 | 80 | 132
Gandak-Rampur | 50 | 25 | 132
Mahendranagar-Tanakpur | 50 | 30 | 132
Kataiya-Rajbiraqj | 10 | 8 | 33
Raxual-Birgunj | 10 | 10 | 33
Sitamadhi-Jaleswor | 10 | 8 | 33
Nepalgunj-Nanpara | 10 | 8 | 33
Jayanagar-Siraha | 8 | 8 | 33

## Slide 14: Large XBTL
Transmission Link | Transfer Cap. (MW) | Voltage Level, kV | Status
Dhalkebar-Muzzafarpur | 1200 | 400 | Under cons.
Bardaghat-Gorakhpur/ Anadnagar | 1200 | 400 | Planned
Duhabi- Jogbani | 1200 | 400 | Planned

## Slide 15: Rational for Regional Trade
System Operational Benefits
  Complementarity in energy demand and energy resource endowments
  Optimal utilization of resources from economies of scale ; Reduced spinning reserves
  Improved energy security
  Reduced environmental impact and climate change imperative
Economic Benefits
  Benefit to smaller exporting economies
  Increased revenues from trade and industrial activities, enhanced industrial productivity
  Significant relief from energy constraints to rapid economic growth
National Benefits
  Implications of trade to energy security
  Reduction of supply costs
    SAPP could realize 45% savings in costs for meeting the same demand if the regional plan is adopted versus the sum of the national power development plans to meet the same demand
  Cash flow implications – the make or buy choice in an environment with competing demands on limited resources
Notes: Countries like India and Pakistan have an almost insatiable appetite for energy that demand is not going to subside any soon

## Slide 16: Way Forward
Greater interaction at both the technical as well as political level to discuss the issues of power trade
Singing PTAs with India asap
SAARC EC work for a inter-governmental MOU
Establishing a Regional Power Trading Regulator
Harmonization of Grid Codes and standards,
Reforming individual country markets to attract greater private sector participation
Joint planning of potential power projects,

## Slide 17
THANK YOU !
THANK YOU
Notes: 17