## Slide 1: Cross-border Power Trade Agreements
Dr Pramod Deo
Ex Chairperson
Central Electricity Regulatory Commission

## Slide 2: In This Presentation…….
Federal Structure
Distribution is mostly in public sector owned by State Govts.
Indian Power Market
Regulatory Initiatives and Outcomes
2

## Slide 3: Installed Generation Capacity in India as on 31.07.2013
Chart: Percentage of Total Installed Capacity
| Thermal | Hydro | Nuclear | Renewable | Total


Total Installed Generation Capacity as on 28.02.2014 is 237.74 GW
Source: CEA
3
Chart: Percentage of Total Capacity
| Thermal | Nuclear | Hydro | Renewable
 | 0.6869 | 0.020106 | 0.16907 | 0.12393
Chart: Breakup of Installed Capacity
| State | Private | Central
 | 0.38461 | 0.33025 | 0.28514

## Slide 4
FLOWGATES
Pan India Market:
All India Economy & Efficiency
Optimal utilization of resources
Well Meshed Network
400 kV Backbone (~100,000 ckt kms)
765 kV Operations commenced
Bulk transfer through HVDCs
High Capacity Corridors under construction
4
Notes: June 27, 2014
NRLDC
4
SLIDE-1: ALL INDIA POWER MAP
· Sir, this picture shows the extra high voltage transmission network in India
· Yellow colour depicts 765 kV lines
· Red colour depicts 400 kV lines and
Purple colour shows plus-minus 500 kV HVDC lines

## Slide 5: Creation of Transmission Highways
NLDC
Cluster of Concentrated Demand pockets
Cluster of Generation pockets

## Slide 6: Growth of Transmission 66 kV and above lines in India
Year | Circuit Km
31.03.1990 | 2,15,903
31.03.1992 | 2,54,613
31.03.2002 | 3,04,258
31.03.2007 | 3,58,580
31.03.2012 | 4,56,055
31.03.2013 | 4,58,529

## Slide 7: Generation Capacity Addition
MW
Chart: 
| 38442 | 38807 | 39172 | 39538 | 39903 | 40268 | 40633 | 40999 | 41305 | 41698
Private gencos | 13688.43 | 14139.2 | 17112.62 | 20010.66 | 22878.75 | 29014.01 | 37496 | 54276 | 62459.24 | 78515.3
Central gencos | 38789.5 | 39923.49 | 45120.99 | 48360.99 | 48970.99 | 50992.63 | 54413 | 59683 | 62963.63 | 67789.94
State gencos | 65941.16 | 70224.48 | 70095.6 | 74689.36 | 76115.67 | 79391.85 | 82453 | 85667 | 86343.35 | 91437.7

## Slide 8: …Private Sector Ownership
Almost 100% of Electricity Transmission in India is owned by public sector
  Is a Regulated monopoly business
  New projects to be awarded through competitive bidding route
About 13 % of Electricity Distribution in India is owned by private sector
8

## Slide 9: Market Breakup 2013-14(upto 31st January 2014)
Bilateral & Power Exchange is 9% of total generation = 70 Billion Units
Unscheduled Interchange is 3 % of total generation= 18 Billion Units
Total Generation = 728 Billion Units ( End of January 2014 )
9
Chart: Share of Different Segments in Total Electricity Generation in 2013-14 (up to January 2014)
| Bilateral | Power Exchanges | UI | Long Term
 | 0.061498 | 0.03492 | 0.025552 | 0.87803
Chart: Share of Different Segments in Short Term Transactions in 2013-14 (up to January 2014)
| Bilateral through traders & PXs | Bilateral between DISCOMs | Power Exchange Transactions | UI transactions
 | 0.3257 | 0.1785 | 0.2863 | 0.20949

## Slide 10
Short Term Market though 9 %, is a $3.18 Billion Market
(1$=61 INR)
Short Term Price and Volume Trends
10
Year | Trader |  | Power Exchange |  | Size of Market through Traders ($Billion) | Size of Market through Exchanges ($Billion ) | Total Size of Short Term Market Excluding UI ($Billion) | Total Volume (BU) (Trader+PX)
 | Volume in Billion Units | Trader Price | Volume in Billion Units | Power Exchange Price |  |  |  | 
 |  | ($/Mwh) |  | ($/Mwh) |  |  |  | 
2008-09 | 21.42 | 119.51 | 2.77 | 122.73 | 2.56 | 0.34 | 2.90 | 24.2
2009-10 | 26.82 | 86.16 | 7.086 | 81.30 | 2.31 | 0.58 | 2.89 | 33.9
2010-11 | 27.7 | 78.53 | 15.52 | 56.45 | 2.18 | 0.88 | 3.05 | 43.2
2011-12 | 35.84 | 68.52 | 15.54 | 58.57 | 2.46 | 0.91 | 3.37 | 51.4
2012-13 | 36.1 | 70.99 | 23.5 | 60.16 | 2.56 | 1.42 | 3.98 | 59.7
2013-14 (till Jan 2014) | 28.4 | 69.81 | 25.4 | 46.99 | 1.98 | 1.20 | 3.18 | 53.82

## Slide 11
Volume of Electricity Transacted through Trading Licensees and Power Exchanges(inter-state transactions)
CAGR of 17.3 % over last 5 years
11
Chart: Volume (BUs)
| 2008-09 | 2009-10 | 2010-11 | 2011-12 | 2012-13 | 2013-14 (till Jan 2014)
 | 24.2 | 33.9 | 43.2 | 51.4 | 59.7 | 53.82

## Slide 12: Recent Regulatory Initiatives and Outcomes

## Slide 13: New Regulations introduced in last two years
Connectivity, Long / Medium term Open Access Regulation
Transmission Pricing Regulation
Pan caking of transmission charges across region removed, level playing field for all in competitive bidding
Renewable Tariff Regulation
Preferential tariff for renewable energy to attract investment in renewable sector
Reduced operational risk for generators, Private and government companies treated equally, improve market access for generators
Sensitive to distance, direction and quantum as prescribed in the national tariff policy
22

## Slide 14
Regulation on Grant of Transmission License
Introduced competitive bidding in transmission
Renewable Energy Certificate Regulation
Helps renewable resource deficit states to meet their statutory RPO
Power Market Regulation
Structured development of short term market , introduction of Power Exchanges, define market rules, and tradable products
Market mechanism for REC Trading
New Regulations introduced in last two years
23

## Slide 15: New Regulations introduced in last two years
Regulation of Power Supply
Payment Security Mechanism for generators & transmission companies
Unscheduled Interchange Regulation
Tighten frequency to improve quality of power
Regulatory Approval to Central Transmission Utility for network augmentation
Help in absorbing intermittent renewable power
Augment transmission along with generation
24

## Slide 16: Daily Maximum & Minimum Frequency in Interstate Grid (1998 onwards)
Maximum
Maximum
Minimum
Frequency Band has been narrowing around 50 Hz
27

## Slide 17: Thank You
Contact: pramoddeo@hotmail.com
+919999002434